## Slide 1
GROUP 12
Estimating River Surface Velocity from Video
Comparing LS-PIV and Optical Flow for Vision-Based Streamflow Estimation
James Welcker • Andrew Chan • Brayden Duerksen • Sean Gilbert
Notes: Intro (≈30 sec): State the project title, group number, and names. One sentence on what the project does.

## Slide 2
01 · MOTIVATION
Why Vision-Based River Velocimetry?
Traditional streamflow gauging (current meters, floats) requires physical river access — slow, costly, and unsafe at high flow.
Video cameras can capture surface motion remotely and repeatedly, at low cost.
Tracking natural tracers (bubbles, foam, ripples) between frames lets us estimate surface velocity without contact instruments.
GOAL
Estimate river surface velocity from ordinary video, then compare it to a known reference velocity.
Extended scope (per proposal feedback): compare two methods, not just implement one.
Notes: Motivation (≈1 min): Why this problem matters and what the project's goal is. Mention the scope expansion from the proposal meeting.

## Slide 3
02 · BACKGROUND
Two Families of Methods
LS-PIV
Large-Scale Particle Image Velocimetry tracks natural tracers (foam, bubbles, debris) between frames — adapting lab-based PIV to outdoor river conditions.
Optical Flow
Estimates a dense field of pixel-level motion using brightness-constancy assumptions, rather than tracking discrete particles.
Key factors affecting both methods: lighting, reflections/glare, motion blur, and how much visible texture is on the surface.
Notes: Background (≈1.5 min): Briefly explain LS-PIV vs. optical flow in plain terms — this is literature-review content, keep it high-level for a general audience.

## Slide 4
03 · METHODOLOGY
From Pixels to Real-World Velocity
1
Capture
Record river surface video with a fixed camera; identify visible tracers (bubbles, foam, ripples).
2
Track Motion
Apply LS-PIV and optical flow separately to estimate pixel displacement between frames.
3
Correct Geometry
Use reference points / homography to convert pixel motion into real-world distance, correcting for camera angle.
4
Compute & Compare
Combine with frame rate to get velocity; compare both methods against a known reference velocity.
Notes: Methodology (≈1.5 min): Walk through the 4-step pipeline. This is a good place to show a diagram or example frame once you have one.

## Slide 5
04 · LS-PIV
LS-PIV — Implementation & Results
IMPLEMENTATION
[How was it implemented? Tools/libraries, key parameters, and any preprocessing steps.]
RESULTS
[Accuracy vs. reference velocity, error metrics (percent error, MAE, RMSE), processing time, and performance under different conditions. Add a chart or example frame here.]
Notes: LS-PIV (≈2 min): Explain how you implemented LS-PIV specifically, then walk through its results — accuracy vs. reference velocity, and how it held up under different conditions. Add a plot or example frame to this slide once available.

## Slide 6
05 · OPTICAL FLOW
Optical Flow — Implementation & Results
IMPLEMENTATION
[How was it implemented? Tools/libraries, key parameters, and any preprocessing steps.]
RESULTS
[Accuracy vs. reference velocity, error metrics (percent error, MAE, RMSE), processing time, and performance under different conditions. Add a chart or example frame here.]
Notes: Optical Flow (≈2 min): Explain how you implemented Optical Flow specifically, then walk through its results — accuracy vs. reference velocity, and how it held up under different conditions. Add a plot or example frame to this slide once available.

## Slide 7
06 · DISCUSSION
Discussion
Which method performed better?
[State which method — LS-PIV or optical flow — was more accurate overall and why. Note any conditions where the other method won instead.]
Trade-offs
[Accuracy vs. processing time, and the impact of the geometric correction step on overall error.]
Limitations
[Dataset size/diversity, reference velocity ground truth quality, and assumptions in the geometric correction.]
Notes: Discussion (≈1.5 min): Mirror the paper's Discussion section — which method won and why, the trade-offs, and the limitations.

## Slide 8
Thank you!
Group 12 — River Surface Velocity Estimation via Computer Vision
James Welcker · Andrew Chan · Brayden Duerksen · Sean Gilbert